Instructions for installation of #306681 and –HP Harmonic balancer bolt kit.

Thank you for purchasing an Atomic bolt kit. To enjoy trouble free operation it is imperative it is installed correctly - failure to follow these instructions will lead to ineffective operation and the possibility of engine damage.

Step 1.

Remove the original harmonic balancer bolt and washer.

Step 2.

Check the face of the balancer and the snout of the crank for irregularities – rectify as required. Run a thread cleaning tap M14/1.5 down the hole if required.

Step 3.

Please note the CRMO washer can be fitted 2 ways, depending on whether the snout of the crank is more than 3mm BELOW the face of the balancer or not.

NOTE: the washer MUST NOT to bottom out on the snout of the crank, so determine which way it faces before proceeding to the next step.

Step 4.

Place some silicone sealer on the keyway of the crank and on the inside face of the washer. Put some thread sealer on the thread of the bolt and torque the bolt to 135 NM. Recheck the torque after one hour.

Remember, if you encounter any problems whatsoever when installing these parts, please call Atomic direct - we are here to help!

Cheers,

The Team at Atomic