Instructions for installation of Atomic Anchorlox® Bolt, Stud/nut and Nut kits

Thank you for purchasing Atomic Anchorlox®. They replace the troublesome OE fasteners that often come loose in high vibration or high heat applications. Our abutment style of locking nut or locking bolt cannot come loose, rectifying this annoying problem. Please note that this Anchorlox® kit has RH threaded nuts or bolts.

To enjoy trouble free operation it is imperative the studs and locknuts are fitted correctly - failure to follow these instructions will lead to ineffective operation and the possibility of engine damage.

Step 1.

Remove the ducting, oil lines, etc to gain access to the item to be secured. Undo the original studs or bolts and inspect the faces for corrosion, warpage etc. Rectify as required. Ensure all threads are free of debris – chase threads as necessary.

Step 2 – Anchorlox STUD AND NUT or NUT kits. Install the studs into the manifold and torque to 25-30 NM (for 8 mm) or 30-35 NM for 10 mm), leaving the longer threaded end protruding from the manifold. The best way to do this is to use the double-nut method. Put Loctite #262 (or equivalent) on the end of the thread before installing in the manifold. Refit the item to be secured (with a gasket if required) and fit the Anchorlox nuts. Tighten to 35-40 NM (8 mm thread), or 40-45 NM (10 mm thread)

Step 2A – Anchorlox BOLT kits. Remove the original fasteners and place a new gasket between the manifold and turbo as required and refit the item with the Anchorlox bolts. Tighten to 35-40 NM (8 mm bolts) and 45-50 NM for 10 mm bolts.

Step 3.

Place an abutment tab over the locknut on the RIGHT HAND SIDE of the body of the turbocharger housing/dump pipe, etc, as viewed from above. Refer Picture above. The tab must be installed in this position so it stops the anti-clockwise rotation (loosening) of the nut/bolt.

NOTE: It may be necessary to file the side of the abutment tabs slightly to allow a tight fit up against the side of the item being secured.

Step 4.

Tap the tab in place and fit the E-clip into the groove of the bolt/nut to retain the tab.

Remember, if you encounter any problems whatsoever when installing these parts, please call Atomic direct - we are here to help!

Cheers, The Team at Atomic