Instructions for Atomic #100790-1 Anchorlox® Locking H/Balancer Bolt kit.

Thank you for purchasing Atomic Anchorlox®. They replace the troublesome OE fasteners that attach a turbocharger to the manifold, as well as other applications where heat and vibration are present.

Our abutment style of locking nut cannot come loose, rectifying this annoying problem. Please note this Anchorlox® kits has RH threads.

To enjoy trouble free operation it is imperative the kit is fitted correctly - failure to follow these instructions will lead to ineffective operation and the possibility of engine damage.

PLEASE NOTE: THIS KIT FITS ATOMIC HARMONIC BALANCERS WITHOUT ANY MACHINING. To fit this kit to a standard or any other brand of balancer it requires drilling and tapping of an M6 thread. Refer Step 5 for details.

Step 1.

Remove the original harmonic balancer bolt and washer and discard. Inspect the face of the balancer for scoring or inadequate flatness – rectify as required.

Step 2. Fit the washer and 12 point bolt to the snout of the crank, using an anti-seize product as lubricant. Torque the bolt to 135 NM. Recheck after 20 minutes.

Step 3.

Place the laser cut abutment tab over the 12 point bolt and slide all the way on – it is a tight fit. Ensure the tab is located in a position where the 6mm hole in the abutment tab is located over the top of one of the drilled and tapped M6 holes in the balancer hub.

Step 4.

Refit the abutment tab to the crank bolt. Place some Loctite 262 on the threads of the M6 Allen head bolt, place the spacer between the abutment tab and balancer, fit the washer under the head of the capscrew, then tighten to 15 NM.

Step 5.

If you are fitting the Anchorlox kit to a standard balancer, the following machining is required. Fit the abutment tab over the bolt so the small M6 end is located above one of the ribs of the balancer. Mark this point on the balancer rib with a centre punch. Remove the abutment tab and drill a 5.25mm hole in the balancer, then tap the hole with an M6 tap. (Drill and tap not included in kit)

Step 6.

Continue as per step 4 above.

Remember, if you encounter any problems whatsoever when installing these parts, please call Atomic direct - we are here to help!

Cheers,

The Team at Atomic