Supplementary installation instructions for #306100-ATI Super Damper

Thank you for purchasing an Atomic/ATI Super Damper. These components have been manufactured using premium quality materials, machined to the highest standards and undergo numerous pre and post production checks to ensure these standards are maintained.

To enjoy trouble free operation, it is imperative the correct installation procedures are followed. Failure to follow these instructions may lead to failure of the component and/or damage to the engine.

To facilitate installation we recommend the following:

Step 1. Check the snout of the crank is free from burrs, nicks, scratches and also inspect the woodruff key for any imperfections – replace if damaged.

Step 2. Heat the HUB ONLY in an oven to 100 degrees C for 30 minutes.

Step 3. Install the hub onto the crank and fit up retaining bolt and washer. This is to be done quickly as the hub will cool and shrink back to its original size, making installation difficult.

NOTE: We strongly recommend the use of a harmonic balancer installing tool. We use ProForm tool #66514.

Step 4. Allow to cool and then torque balancer hub to specs (135NM) and use a small amount of silicone sealer on the inside face of the washer to stop oil migration along the keyway.

Step 5. Fit Super Damper assembly to the hub using the ATI bolts supplied. Torque to the specs contained in the ATI instructions – 15-18 ft. lbs for 5/16” bolts and 28-30 ft. lbs for the 3/8” bolts.

If you encounter any problems whatsoever with the installation of our parts or have any questions about DOHC Ford 6 cylinder engines in general, please call Atomic direct - we are here to help!

The Team at Atomic

2/2019 updated 5/2022