Installation instructions and specifications for Atomic O-Ringed Head Gasket.

Thank you for purchasing an Atomic Performance Product. It has been manufactured using premium quality materials, machined to the highest standards and undergoes numerous pre and post production checks to ensure these standards are maintained. To enjoy trouble free operation it is imperative the correct installation procedures are followed. Failure to follow these instructions may lead to failure of the component and/or damage to the engine.

Step 1

Remove the cylinder head and inspect for flatness, suitable Ra finish and corrosion around the water passages. Rectify as required.

Step 2

Check the deck face of the block for flatness. Inspect the M12/1.5 threaded holes to ensure the threads are clean and the thread-form is not damaged. Rectify are required.

Step 3.

Install the 2 head to block dowels and then install head studs in accordance with the Manufacturers recommendations.

Step 4.

Place a small bead (approx 1mm dia) of sealer around the water and oil passages on the block. Repeat with the corresponding passages in the cylinder head. There is no need to put any sealer around the O-Ring chambers of the gasket.

Step 5.

Check the head gasket is not damaged and then place it on the block, pushing down lightly so as to spread the bead of sealer. Place the head over the studs and onto the gasket.

Step 6.

Continue the installation of the head studs in accordance with the Manufacturers recommended method. Reinstall valvetrain, etc.

Step 7.

Restart the engine and check for leaks. Check coolant and oil levels and adjust as required. After the engine has reached operating temperature, run for another 15-20 mins then shut down motor and check the torque of the head studs. Slight retorquing may be required at this time. Repeat this process once motor has cooled completely.

If you encounter any problems whatsoever with the installation of our head gasket or have any questions about DOHC or SOHC Ford 6 cylinder engines in general, please call Atomic direct - we are here to help!

The Team at Atomic

5/2016