Instructions for Atomic billet steel crankshafts - #306174-DS and -SS.

Thank you for purchasing a quality Atomic billet crankshaft. To enjoy trouble free operation it is imperative the crank is installed correctly - failure to follow these instructions will lead to ineffective operation and the possibility of severe engine damage.

Detailed below are answers to frequently asked questions regarding crank installation.

Pre installation checks

- Remove the crank from the packaging and check for damage to the crank.

- Pay careful attention to the journals, snout and rear main seal area.

- Please note the journals are ground to standard Ford diameters.

- Ensure all oil galleries are clear of any debris, grease, etc. A gun rifling brush with solvent and compressed air is a favoured method to ensure all passages are clean and clear.

- Check the M14/1.5 thread in the end of the crank is not damaged.

Balancing.

The crank is balanced to within our specifications, however re-balancing can be undertaken, depending on the intended usage of the engine. It is entirely up to the discretion of the engine builder.

Bearing clearances

Clearances are to be determined by the engine builder and the application the crank will be used in. As a general rule, allow at least .0015” clearance on the conrod journals, .003” main bearing clearance and a minimum of .005” end float.

Flywheel/flexplate Dowelling

Dowelling of the flywheel is recommended. We suggest a minimum of 3 x M10 dowels. We have a tool available to undertake dowelling (#100709) or we can dowel it for you for an additional charge.

Spigot bearing

Our billet cranks are not supplied with a spigot bearing, however provision is made for installation of a bearing. If the crank is to be fitted with a manual transmission we suggest the use of the genuine Ford roller spigot bearing – part # D4DZ 7600A.

Remember, if you encounter any problems whatsoever when installing these parts, please call Atomic direct - we are here to help!

Cheers,

The Team at Atomic