Instructions for installation of #306504 Power Steer pump delete/idler kit.

Thank you for purchasing an Atomic power steering pump delete/idler kit. To enjoy trouble free operation it is imperative these instructions are followed carefully – failure to do so could lead to ineffective operation and the possibility of severe engine damage.

Step 1.

Remove the power steer pump.

Step 2.

Affix the alloy mounting bracket to the timing cover as per the picture to the right. Torque the M8 bolts to 25 NM with washers and flange nuts.

Step 3.

Mount the idler pulley and to the bracket by way of the M12 flange bolt provided. Torque nylock nut to 35 NM.

Step 4.

Refit the belt to run in the same direction and location as original. Recheck after one hour’s operation.

NOTE: In some unusual cases it may be necessary to use a 10mm shorter belt than listed below.

Belt length table

| Balancer | Alternator | H2O pump | Pump options | Belt Length |
| --- | --- | --- | --- | --- |
| Stock Ford balancer | BA | Stock | With aircon compressor | 6PK2190 |
| Stock Ford balancer | BF-FG | Stock | With aircon compressor | 6PK2220 |
| Stock Ford Balancer | BA | Stock H2O pump | Ford P/steer pump fitted | 6PK1630 |
| Atomic Race balancer – std speed | BA | Stock H2O pump | Ford P/steer pump fitted | 6PK1640 |
| Atomic Race balancer – 15% underdrive | BA | Stock H2O pump | Ford P/steer pump fitted | 6PK1580 |
| Atomic Race balancer – 15% underdrive | BA | No H2O pump | Ford P/steer pump fitted | 6PK1300 |
| Atomic Race balancer or STD balancer. | BF/FG | Stock H2O pump | Ford P/steer pump fitted | 6PK1640 |
| Atomic/ATI SuperDamper | BF/FG | No H2O pump | No power steer - #Atomic #306504 delete fitted | 6PK1300 |
| Stock Ford balancer | BF-FG | Stock H20 pump | Atomic #306503 Aircon delete and #306504 Power steer delete kits fitted. | 6PK1625 |

Remember, if you encounter any problems whatsoever when installing these parts, please call Atomic direct - we are here to help!