Instructions for installation of Atomic #306562 Billet crankshaft sprocket.

Thank you for purchasing an Atomic billet steel crankshaft sprocket to suit a Ford 6 cyl engine. To enjoy trouble free operation it is imperative it is installed correctly - failure to follow these instructions will lead to ineffective operation and the possibility of severe engine damage.

Step 1.

Remove the harmonic balancer and timing cover from the engine to expose the camshaft drive system.

Step 2.

Rotate the engine to TDC with the timing chain marks lined up, then engage the lock pin on the timing chain tensioner and remove the timing chain.

Step 3.

Remove the crank sprocket by sliding it off the snout of the crank. This can usually be accomplished by hand in most occasions, however sometimes a puller may be required.

Step 4.

Check the snout of the crank and the woodruff key for nicks or damage. Replace the key if required. Also check the new sprocket carefully for nicks or damage. Place the sprocket onto the snout of the crank and with a light tapping motion with a rubber hammer, gently tap the sprocket into place.

Step 5.

Refit the timing chain and time up as per OE. Please note all timing marks on our sprocket correspond with the factory marks. Refer pictures of both timing marks with RED arrows.

Step 6.

Release the timing chain tensioner and rotate the engine over a few times to ensure the chain rotates smoothly.

Step 7.

Refit the timing cover and external accessories in the reverse method of disassembly.

Remember, if you encounter any problems whatsoever when installing these parts, please call Atomic direct - we are here to help!

Cheers,

The Team at Atomic