Atomic Billet cam suit Ford 4.0L AU SOHC engine

– Stage 3 Turbo/blown

Camshaft profile information and installation instructions.

#306590-3 - Custom ground inverted flank asymmetrical roller billet camshaft

- Advertised Inlet duration – 282 degrees

- Advertised exhaust duration – 282 degrees

- Duration at .050” lift – 222 degrees inlet and exhaust

- Cam phasing - suggest set up at .120” INLET VALVE Lift @ TDC)

- Lobe lift – .284” (both)

- Lobe centres – 115 degrees

Timing figures - at .050” lift

IO – (minus) 2 degrees after TDC

IC - 44 degrees after BDC

EO - 48 degrees before BDC

EC – (minus) 6 degrees before TDC

Duration: 220 degrees inlet and exhaust

Rocker arm ratio: 1.80:1 Theoretical valve lift: .504” with zero tappet clearance

All Atomic cams are ground on new billets and have standard base circle dimensions.

Installation instructions – SOHC  engines.

- Remove turbo ducting (as applicable) to gain access to rocker cover. Remove cover etc to gain access to valvetrain.

- Rotate engine until the timing marks on timing chain line up with marks on camshaft sprocket, then loosen cam saddles carefully.

- Secure the timing chain against the side of the timing cover with a piece of wire. Please note the timing chain tensioner will extend fully at this time, however it can be easily reset later.

- Measure the bearing journals of the cams being removed and compare against the new cams – the new cams must be within .001” of the original camshaft diameters. We have noted a lot of variation in factory camshaft tunnel/cam sizes, so pay particular attention to these sizes. In some cases it may be necessary to reduce the diameter of the new cams’ journal to match that of the cam being removed.

- Check and inspect the condition of the roller followers/rockers for signs of wear and replace as necessary.

- Check valvespring tensions and replace any weak springs with suitable replacement springs as required.

- Reinstall the new camshaft and install 2 lifter and rocker assemblies and check the amount of lifter preload/clearance that exists. Bleed down the lifters and check that the lifter has no less than .4mm preload or no more than 1.0mm. Shim lifters as required to achieve desired preload, applying a liberal coating of engine oil to all contact surfaces.

- Refit the timing chain and reset the timing chain tensioner to the fully retracted position paying careful attention the timing marks on the sprockets are lined up correctly with the timing chain.

- Release the timing chain tensioner and set in place.

- Degree in the cam, noting our suggested valve lift at TDC figures.

- Continue to reinstall the rest of the components and torque all bolts to the factory specifications.

- To verify the timing marks are correctly lined up, rotate the engine until the timing marks come back around and correspond with the camshaft sprocket.

- Reinstall the rest of the engine accessories and double check all bolts, clamps, etc are tight. Restart engine and hold at an idle speed of 1000-1400 RPM for 10 minutes.

Important notes.

- Engine will require tuning to get the maximum benefit from the camshafts’ extra breathing capacity.

- If the vehicle is driven any great distances before tuning is carried out the OBD system may log a fault code due to the new camshafts altering the engine vacuum. If this occurs the code can be reset by the tuner.

- The camshafts do not require any run in period.

- Ford lifters can take up to 45 minutes of running before they bleed up correctly – be patient and keep the engine RPM low until the running clearance is taken up by the lifter.

- If you have any questions, please do not hesitate to call us – we are here to help!!

The Team at Atomic