Instructions for installation of #306700, etc piston rings to suit Atomic and Cosworth F1 Series pistons, etc.

Thank you for purchasing Atomic Performance piston rings. To enjoy trouble free operation it is imperative the rings are installed correctly - failure to follow these important points will lead to ineffective operation and the possibility of severe engine damage.

Point 1.

It is strongly recommended that a torque plate be used when finishing cylinder sizing to produce a concentric and straight bore when the cylinder head is torqued on place. Suggested plateau finishing is with a #320 grit stone.

Point 2.

Check the rings in the piston grooves to ensure sufficient back and vertical clearance exists. If fitting the rings to used pistons, please ensure the ring grooves are clean. Please note the STEEL TOP RINGS are bright silver finish – the SECOND rings are black.

Point 3.

The rings are FILE-TO-FIT and must be checked individually and the end gaps filed to suit each individual bore. We recommend a minimum clearance of .006” per inch of bore diameter for the top compression rings (steel) and .0065” for the second compression ring (iron) for all applications, including forced induction. The dot on the second ring is to go UP. We recommend a minimum end gap of .024” for top and second rings.

Point 4.

The oil rings are made up of 3 pieces – a central wavy expander and 2 stainless rails. The expander end gap is adjusted by bending the tips of the expander to provide the correct clearance, with a minimum of .005”. The minimum gap for the oil ring rails is .015” Use 30W engine oil as the lubricant for the rings.

Point 5.

The positioning of the end gaps is as follows (as viewed with the piston installed in the engine):

- TOP RING: 5 O’clock

- SECOND RING: 10 O’clock

- TOP RAIL: 2 O’clock

- EXPANDER: 7 O’clock

- LOWER RAIL: 4 O’clock

Point 6.

Use of a tapered ring installer is the best method to install the pistons however a pliers-type ring compressor will also work OK.

Remember, if you encounter any problems whatsoever when installing these parts, please call Atomic direct - we are here to help!

Cheers,

The Team at Atomic