Instructions for installation of #306720 Chrome Moly Flexplate kit.

Thank you for purchasing an Atomic flexplate to suit a Ford AU-on 6 cyl engines fitted with M10/1.25 bolts. To enjoy trouble free operation it is imperative the flexplate is installed correctly - failure to follow these instructions will lead to ineffective operation and the possibility of engine and/or gearbox damage.

Step 1.

Remove the gearbox from the car, and then remove the original flexplate from the vehicle.

Step 2.

Check the flange of the crankshaft is free of damage or burrs – dress lightly with a stone if required. Carry out the same checks on the rear of the flexplate. Ensure the threads in the crank are in good condition and check they are at least 20mm deep. Run a M10 x 1.25mm bottoming tap down the holes if required.

Step 3.

Check the bolt pattern on the torque converter lines up with the bolt pattern on the flexplate. If in doubt, please call Atomic directly.

Step 4.

Fit up the flexplate to the crank, noting that the 6 bolt PCD is not evenly spaced at 60 degrees each. Rotate the flexplate on the crank flange until the holes line up and lubricate the undersides of the Allen head bolts and the spot faces of the flexplate with a small amount of moly lubricant.

Step 5.

Place a locking washer under the heads of the Allen head bolts. Place Loctite #262 (or equivalent) on the threads. Torque the bolts to 100 NM (75 ft lbs). Recheck the torque after 15 minutes. Repeat on all bolts.

Step 6.

Refit the gearbox and the torque converter in the reverse order of removal, ensuring the torque converter engages the pump drive correctly. Longer M10/1.25 bolts have been supplied with the flexplate kit and are to be torqued to 65 NM (46 ft.lbs). Please note that some torque converters have a larger bulge at the rear – make sure there is clearance between the bolts and the back of the converter.

Step 7.

Check the heads of the torque converter bolts do not contact the inspection hole in the sandwich plate – adjust as required. Refit the starter, etc then start the car and check for leaks.

NOTE: Variations in torque converter mounting lugs in BF-FG Ford 6 cyl engines.

We have recently noted that the outside diameter of the mounting lugs on certain Ford torque converters are larger than others, so therefore it may be necessary to remove 1.00-2.00 mm from the outside of the mounting foot to allow fitment of the mounting lug against the face of the flexplate.  This is easily accomplished with simple hand tools.

Remember, if you encounter any problems whatsoever when installing these parts, please call Atomic direct - we are here to help!

Cheers,

The Team at Atomic