Installation instructions for #306751, #306751-S and #306751-RB Ford DOHC 6 cylinder oil pumps.

Thank you for purchasing a quality Atomic product. It has been manufactured using premium quality materials, machined to the highest standards and undergoes numerous pre and post production checks to ensure these standards are maintained. To enjoy trouble free operation it is imperative the correct installation procedures are followed. Failure to follow these instructions may lead to failure of the component and/or engine damage.

PLEASE NOTE: It is advised the installation of this product is best undertaken if the motor is not fitted to the car. The installation can be carried out if the engine is fitted to the vehicle; the crossmember must be dropped and the engine supported so as to gain access to the sump, which has to be removed.

Step 1.

Remove the sump and pickup from the engine and then remove the timing cover.

Step 2

Remove the timing chain, noting the position of the yellow timing marks in relation to the cam and crank sprockets. Remove the crank sprocket and check for wear on the teeth.

Step 3.

Remove the oil pump and thoroughly degrease the front of the engine. Put a very small amount of flange sealer (such as Loctite 515, Stag, Hylomar, etc) around the face of the pump outlet and the chain oil feed, allowing it to dry in accordance with the instructions. There is no gasket for these areas, so please use sealer sparingly. PLEASE NOTE: This step is not required on the oil pump outlet port on #306751-S pumps as we have O-ringed the outlet flange and supplied the appropriate O-ring. Fit the pump to the motor using the supplied M6 capscrew bolts and tighten to the factory torque specification of 10-12 Nm. Check the pickup is clean and fit the Viton oil pickup o-ring (also supplied with the pump) using a small amount of grease as a lubricant and re-fit the pickup. Ensure the correct length bolts M6 x 20 mm UHL flange bolts (supplied) are refitted to the pump pickup – too long a bolt can damage the pump body or compromise the ability of the pickup O-ring to seal.

PLEASE NOTE: There is no need to strip and inspect our pump before fitting to the engine - it has been tested and is primed and ready to go as is.

Step 4.

Check there is no debris in the sump and then refit the rest of the engine components in the reverse order of removal, paying close attention to the timing of the camshafts. Please note a small dab of sealer is all that is needed in the corners of the O-ringed/gasketed faces such as early model (pre 5/2005) engine timing cover and sump rails. Use your preferred RTV sealer in other applications such as the timing cover, etc as required and use sparingly.

Step 5.

Prefill the oil filter and allow oil to soak in before fitting to the engine – this may take 2-3 attempts before the filter is actually full. Fill the sump and fit a mechanical oil pressure gauge before starting engine. If the motor has standard bearing clearances it should have a minimum of 25-30 psi at 2000 RPM (hot). The pressure will be higher with cold oil. Check engine for oil leaks and recheck oil level.

If you encounter any problems whatsoever with the installation of this product, please call Atomic direct on 02-8665 5889 or email us at sales@atomicperformanceproducts.com - we are here to help!