Installation instructions - #306753 Billet steel oil pump end plate kit to suit

Ford DOHC Ford 6 cyl.

Thank you for purchasing Atomic oil pump end plate kit. To enjoy trouble free operation it is imperative it is installed correctly - failure to follow these instructions will lead to ineffective operation and the possibility of severe engine damage.

Step 1.

Remove the oil pump from the engine and remove the rear cover plate. This will require the use of an impact driver with a Phillips head tip.

Step 2.

Remove the original gerotor pump gears and inspect the inside of the pump housing for scoring. Discard and replace the housing if wear marks are more than .5mm deep.

Step 3.

Lubricate the inside of the oil pump housing with oil and refit fit the outer gear. Ensure it rotates easily by hand and then lubricate the inside with petroleum jelly. Lubricate the teeth of the internal gear with petroleum jelly also and install in the external gear. Rotate the gears by hand to make sure they revolve smoothly inside the pump.

Step 4.

The packing of the gears with petroleum jelly is to provide a seal for the pump to create a vacuum upon starting, thereby drawing oil into the pump.

Step 5.

Fit the oil pump cover plate and tighten the Allen head screws (provided) to 12NM. Use Loctite #222 or equivalent on the threads

Step 6.

Refit the pump in the reverse order of removal and fit to the engine with a very small amount of non-hardening sealer on the outlet port and the timing chain oil feed passage. Fit a new oil pump O-ring to the pickup tube – Atomic part # 306031. You must use a VITON O-ring in this application – a conventional rubber or Buna-N O-ring cannot be used.

Remember, if you encounter any problems whatsoever when installing these parts, please call Atomic direct - we are here to help!

Cheers,

The Team at Atomic