Installation instructions for Atomic VCT Solenoid delete kit #306761-PR.

Thank you for purchasing a quality Atomic product. It has been designed to eliminate the VCT solenoids in Ford Barra 6 cyl engines that do not use the factory VCT sprockets. They are for use with cylinder heads that accept 20mm solenoids only – they do not fit First Gen (BA style) heads with 18mm solenoids.

To enjoy trouble free operation it is imperative the correct installation procedures are followed. Failure to follow these instructions may lead to failure of the component and/or damage to the engine.

Step 1

Remove the camshaft sprockets, then remove the factory solenoids and check the internal passages of the camshaft caps for any burs, nicks, etc. Rectify as required.

Step 2.

Remove the retaining cap, O-ring and M6 countersunk bolt from the spigot body. Lubricate the 2 O-rings and install the spigot body into the solenoid tunnel from the rear of the cap (as per photo).

Step 3.

Lightly lubricate the O-ring and push it into the camshaft tunnel, up against the back of the main body of the spigot.

NOTE: The design of the blanking spigot is for the third O-ring to expand when the cap is fitted, securing the spigot in place.

Step 4.

Place some non hardening thread sealer on the threads of the M6 bolt and fit with the retaining cap to the spigot. Tighten to 12 NM. Note: There are flats machined into the opposite end of the spigot to stop rotation when tightening the M6 countersunk bolt.

Step 5.

Refit camshaft drive components in reverse order of removal.

Note: It is recommended to also fit a set of Atomic #306760 Rocker Cover blank off plates to complete the installation in a professional manner.

If you encounter any problems whatsoever with the installation of these parts or have any questions about DOHC or SOHC Ford 6 cylinder engines in general, please call Atomic direct - we are here to help!

The Team at Atomic