Instructions for installation of #306901 Viper Intake manifold and dual feed fuel rail kit.

Thank you for purchasing an Atomic intake manifold to suit a Ford 6 cyl engine. To enjoy trouble free operation it is imperative it is installed correctly - failure to follow these instructions will lead to ineffective operation and the possibility of engine damage.

Step 1.

Remove the factory inlet manifold, including the fuel rail and injectors.

Step 2.

Remove the thermostat housing and remove the casting flash from the rear face of the housing. This will allow the blanking nut on the end of the Viper fuel rail to clear the housing. Clean the inlet port flange of the head to remove residual gasket debris, etc.

Step 3.

Bolt the manifold in place and torque the fasteners to the factory torque specification of 20Nm, using Loctite on the threads.

Step 4.

Fit up the fuel rail and your injectors. Please note the fuel rail is designed to accept conventional length 14mm x 14mm injectors. Mount your fuel pressure regulator in a position where easy access is available to the pressure adjustment and connect it to the centre outlet port in the fuel rail. Connect fuel pressure to BOTH ends of the fuel rail.

Step 5.

Fit up your throttle body using the adaptor/spacer supplied. The DBW motor is to the rear of the manifold. Connect up your intercooler piping to the throttle body in the same manner as originally installed. Connect up all other relevant vacuum and boost pressure ports, making sure a one way valve is fitted between the manifold and the PCV valve to stop boost pressure from entering the crankcase. Start the car and check for leaks. If all is OK, retune the vehicle to suit the new manifold’s flow characteristics.

Remember, if you encounter any problems whatsoever when installing these parts, please call Atomic direct - we are here to help!

Cheers,

The Team at Atomic