Installation instructions for #356735 Idler link bar kit.

Thank you for purchasing a quality Atomic product. It has been manufactured using premium quality materials, machined to the highest standards and undergoes numerous pre and post production checks to ensure these standards are maintained. To enjoy trouble free operation it is imperative the correct installation procedures are followed. Failure to follow these instructions may lead to failure of the component and/or engine damage.

Step 1.

Rotate the engine until it reaches TDC firing and then remove the timing belt cover to gain access to the cam belt idlers.

Step 2.

Loosen the nuts and the bolts securing the idlers in place and remove from idlers the engine. Using a stud remover, undo the idler stud and discard. Check the threads in the block are in good condition and free from debris, etc. Make good the threads by way of a Helicoil, if required.

Step 3.

Reinstall the idlers in the same positions as original, using the bolts and hardened washers supplied in the kit and adjust the idlers to provide the desired belt tension.

Step 4.

Install the link bar to the mounting bolts with the 5mm Allen head bolts provided and tighten securely. Ensure sufficient clearance exists between the underside of the idler link bar and the idlers so they may turn freely on their axis. In some cases, it may be necessary to install a flat washer between the idler link bar and the idlers. This is due to the fact there is a number of manufacturers of idlers and the dimensions vary.

If you encounter any problems whatsoever with the installation of this product, please call Atomic direct on 02-9075 0998 - we are here to help!