Cylinder Head Torque Sequence

Please refer to the manufacturer of the fasteners and the gasket you are using for the relevant torque specifications.

Atomic Head Gasket part numbers/torque specs

#306161-SLS - using 12mm Tool Steel Head Studs, torque to 110 ft.lbs and use VHT Copper Coat sealer on both sides.

#306161-MLS – using 12mm Tool Steel Head Studs, torque to 110 ft.lbs and use VHT Copper Coat sealer on both sides.

#306168-OR using 12mm Tool Steel Head Studs, torque to 110 ft.lbs and use Wurth Silicone 250 (or equivalent) around coolant and oil passages

#306169-KF Fire Ringed head gasket kit - using M13.4mm Tool Steel Head stud kit, torque to 135 ft.lbs and use Wurth Silicone 250 (or equivalent) around coolant and oil passages.

If you encounter any problems whatsoever with the installation of this product, please call Atomic direct on 02-8665 5889 - we are here to help!

Cheers,

The Team at Atomic