Installation instructions and specifications for #306850, #306851 etc Competition Valvespring retainers.

Thank you for purchasing a set of Atomic Competition Valvespring retainers. They have been manufactured using premium quality materials, machined to the highest standards and undergo numerous pre and post production checks to ensure these standards are maintained. To enjoy trouble free operation it is imperative the correct installation procedures are followed. Failure to follow these instructions may lead to failure of the component and/or damage to the engine.

Step 1

Remove the retainers from their packaging and check the correct number are included – 24. If not, please contact Atomic directly on (02) 8665 5889.

RETAINER SPECIFICATIONS

| Part Number | To suit | Material | O.D | I.D | Installed Height |
| --- | --- | --- | --- | --- | --- |
| #306850 | DOHC | Chrome moly | 23.45mm | 15.98mm | +1.25mm |
| #306851 | DOHC | Titanium | 23.45mm | 15.98mm | Std |

NOTE: It is the responsibility of the installer to ensure the correct spring and retainer is used for the particular application. Consideration must be given when the cylinder head, valves and/or valve seats have been machined. It is not recommended that a straight wound spring be used in DOHC engines as premature fatigue will result. If in doubt, please call Atomic direct.

Step 2.

All Atomic retainers are machined to accept the std collets or Atomic collets, Springs for DOHC engines are CONICALLY wound, as per the factory spring design. This is to provide the correct spring pressures whilst fitting both the spring base (larger diameter at bottom) and the factory spring retainer (smaller diameter at top) correctly. Install the springs in this manner, using the appropriate retainer to achieve the desired tensions.

If you encounter any problems whatsoever with the installation of our springs or have any questions about DOHC or SOHC Ford 6 cylinder engines in general, please call Atomic direct - we are here to help!

The Team at Atomic